Open Trench Audit Report (Civil, Electrical & Cable Hauling)

| Project Details |
| --- |
| Network # |  |
| PM Order # |  |
| Project name/stage |  |
| Project location |  |
| CP/PAL approved drawing/s # |  |
| Project type | Network Managed (Option 1) Customer Managed (Option 2) Residential Residential Industrial/Commercial Industrial/Commercial Public Lighting Public Lighting Network Initiated |
| Project scope |  |
| Project Stakeholders |
| CP/PAL Network Project Manager | Name: |
| Customer Project Manager (PM1/PM2) | Company: Name: Phone: Email: |
| Electrical Constructor | Company: Name: Phone: |
| Civil Contractor | Company: Name: Phone: VEDN #: VEDN Expiry: |
| Worksite Civil Auditor | Name: Phone: VEDN #: |
| Worksite Electrical Auditor | Name: Phone: VEDN #: |
| Worksite Cable Hauling Auditor | Name: Phone: VEDN #: |
| Cable Detailer (URD & UG projects only) | Company: Name: Phone: Cable details drafting company (if different from above): |

| PART 1: Open Trench – Civil (prior to cables being installed in trench) (must comply with VEDN requirements) |
| --- |
| INSPECTION ITEM GUIDELINES | Comp y/n/na | Inspect. Date | Initials | Comments |
| Design specification |
| Approved construction drawing provided (current) |  |  |  |  |
| SITE REFERENCES |
| Lot title boundaries pegged |  |  |  |  |
| Kerb & channel installation complete |  |  |  |  |
| Final surface levels can be determined |  |  |  |  |
| TRENCH |
| WIDTH - To design specification e.g. shared use |  |  |  |  |
| DEPTH - Compliant with plan and final surface level |  |  |  |  |
| OFFSET - Alignment correct |  |  |  |  |
| DEVIATION - No unapproved route deviations |  |  |  |  |
| JOINT HOLES – correct size |  |  |  |  |
| BEDDING SAND |
| Correct depth when compacted (min 100mm) |  |  |  |  |
| Correct grade/type |  |  |  |  |
| Free of rocks, sharp or foreign objects |  |  |  |  |
| SERVICE PITS |
| Location – correct boundaries |  |  |  |  |
| Entry conduits installed (75mm +/- 25 mm into pit) |  |  |  |  |
| Body not distorted, lid fitted & operational |  |  |  |  |
| CONDUITS |
| Correct size and category |  |  |  |  |
| DEPTH - Compliant with plan and final surface level |  |  |  |  |
| Road crossing Telco separation (100mm LV /300mm HV) incl. tape |  |  |  |  |
| Separation to other utilities (as specified by Network Owner) |  |  |  |  |
| Spare/future conduits capped or sealed |  |  |  |  |
| Road crossing – warning tape installed & 150mm above conduit |  |  |  |  |
| Warning tape other areas (300mm -50/+150mm from FSL) |  |  |  |  |
| AS BUILT DETAILS |
| Supporting digital photographs recorded/attached |  |  |  |  |
| Asset details recorded prior to cover/backfill |  |  |  |  |
| Recognised Cable Detailer - name and company responsible |  |
| SUBSTATION RESERVE (Where specified) |
| Free of all other authorities’ underground assets |  |  |  |  |
| Site flat and level |  |  |  |  |
| Substation site dimensions as per Standard |  |  |  |  |
| If specified: retaining wall, batter & drainage installed |  |  |  |  |
| Foundation culvert installed correctly and level as per Standard |  |  |  |  |
| Foundation located correctly within substation site |  |  |  |  |
| NOTES (attach extra sheets as required) |
| Note: All non-compliances must be rectified or variations approved by Network Owner Project Manager prior to submission of the completed Civil and Electrical Open Trench Audit Report. |
| DECLARATION |
| The above project COMPLIES / DOES NOT COMPLY with all relevant Network Technical Standards and approved drawings at the time of audit inspection. |
| Approved Worksite Civil or Electrical or Network Auditor |
| Audited by |  | VEDN # |  |
| Signature |  | Date |  |

| PART 2: Open Trench – Electrical (cables installed in open trench prior to cover or backfill) |
| --- |
| INSPECTION ITEM GUIDELINES | Comp y/n/na | Inspect. Date | Initials | Comments |
| DESIGN SPECIFICATIONS |
| Approved construction drawing provided (current) |  |  |  |  |
| Specifications provided for all cables and equipment |  |  |  |  |
| Specifications provided for decorative (non-std) lighting |  |  |  |  |
| Open Trench Audit Report - Civil completed |  |  |  |  |
| Items for follow-up Open Trench Audit-civil completed |  |  |  |  |
| SITE STATUS |
| Cable sand and slabbing completed |  |  |  |  |
| Kiosk sub, cabinets & pillars installed |  |  |  |  |
| Service pits & PL columns installed |  |  |  |  |
| Cable joints and terminations completed |  |  |  |  |
| Telco pipes and pits installed |  |  |  |  |
| CABLES |
| Type and size as specified on plan |  |  |  |  |
| DEPTH - Compliant with plan and final surface level |  |  |  |  |
| OFFSET – Correct as specified on plan |  |  |  |  |
| Laid in correct order & with correct circuit separation |  |  |  |  |
| Bending Radius |  |  |  |  |
| Cable lengths for termination/joints inc. marker pits |  |  |  |  |
| JOINTS & TERMINATIONS (including KIOSKS & P/PILLARS) |
| Joints located >5m from any property boundary |  |  |  |  |
| Cable sealed/insulated ends located as per plan |  |  |  |  |
| Joints completed |  |  |  |  |
| Terminations & P/Pillars satisfactory (CHPs, Pillars, Kiosks) |  |  |  |  |
| CLEARANCE TO OTHER ASSETS |
| Horizontal/parallel or crossing/vertical clearances compliant |  |  |  |  |
| Position for future Telco installation |  |  |  |  |
| Shared trenching - separation to Telco pipes and pits. |  |  |  |  |
| Correct separation - common trenching with other assets |  |  |  |  |
| SAND & SLAB |
| Correct depth when compacted |  |  |  |  |
| Correct grade/type |  |  |  |  |
| Free of rocks, sharp or foreign objects |  |  |  |  |
| Protective slabs installed correctly |  |  |  |  |
| SERVICE PITS |
| Location – correct boundaries |  |  |  |  |
| Entry conduits installed (75mm +/- 25 mm into pit) |  |  |  |  |
| Body not distorted, lid fitted & operational |  |  |  |  |
| Footpath encasement |  |  |  |  |
| Cables terminated correctly |  |  |  |  |
| PUBLIC LIGHTING |
| Poles correct setting depth and straight |  |  |  |  |
| Internal wiring and earthing correct |  |  |  |  |
| Offsets as specified – BOK etc |  |  |  |  |
| Decorative lighting as per drawing specifications |  |  |  |  |
| SUBSTATIONS |
| Substation complies with all drawing specifications |  |  |  |  |
| Earthing to correct standard |  |  |  |  |
| Kiosk placed correctly on foundations and level |  |  |  |  |
| Signage & labelling correct |  |  |  |  |
| AS BUILT CABLE DETAILS – Part 1 |
| Supporting digital photographs recorded/attached |  |  |  |  |
| Asset details recorded prior to cover/backfill |  |  |  |  |
| Recognised Cable Detailer - name and company responsible |  |

AS BUILT CABLE DETAILS – Part 2

Record UG cable location as-built details on the As Built Cable Details table below as follows: Minimum 2 checks on each LV circuit per street plus HV, with inspections not to exceed 100m between points. It is preferred that one of the points includes a service tee-joint, mains tee-joint or a cable turning point where applicable. Note: All HV/LV mains cables are to be recorded at each inspection.

| NON-COMPLIANCES (Indicate status as follows) |
| --- |
| (R) Rectification confirmed during or at completion of audit |
| (F) Follow up inspection required for a Compliant Audit (if applicable) – Exact location with dimensions to be specified |
| (V) Variation approval received from Network Owner Responsible Officer (Attach or provide details) |
| NOTES (attach extra sheets as required) |
| Note: All non-compliances must be rectified or variations approved by Network Owner Project Manager prior to submission of the completed Civil and Electrical Open Trench Audit Report. |
| DECLARATION |
| The above project COMPLIES / DOES NOT COMPLY with all relevant Network Technical Standards and approved drawings at the time of audit inspection. Inspections have been conducted in accordance with the CitiPower/Powercor Open Trench Audit Guideline and/or Work Instruction as applicable, documents JEQA4UJ443MT-160-95 (12-15-G0015) & JEQA4UJ443MT-150-348 (12-15-W0002). |
| Approved Worksite Electrical or Network Auditor |
| Audited by |  | VEDN # |  |
| Signature |  | Date |  |

As Built Cable Details (Sample Inspection Record)

| Asset Description - Circuit / Street name | Measurements |
| --- | --- |
|  | Chainage | Offset | Depth |
| eg. LV service tee joint. West cct. Simmons St, north side | 5.35m from Lot 107/109 boundary | 2.70m from property (4.65m BOK) | 680mm |

| PART 3: Cable Hauling Checklist |
| --- |
| TRAINED/QUALIFIED CREWS ON SITE |
| Name of Crew Leader onsite |  |
| Names of trained Cable Haulers (min 2) |  |
| Items to be checked Inspections Notes / Comments / Rectifications Use extra lines if required Note if item not applicable (N/A) to task being audited Yes No OPEN TRENCH – Civil audit is COMPLIANT The Approved Drawing by Network owner is onsite Cable Haul type:- Direct Manual Winch Bonded Flaking Caterpillar CABLE DRUM SET UP Self loader Cable stands Flatbed truck / stand Position of TRUCK / CABLE DRUM appropriate to cable haul Exclusion zone in place around winch / Operator protection Rope and cable haul free from other assets to avoid damage etc. Position of WINCH - ‘Directly in-line with Trench’ where possible ROLLERS STRAIGHT RUNS – (Cable Clear of Soil/Sand) CORNERS min. 3 rollers pinning / blocking out (Allowance for Tension on corner rollers considered) DRUM to TRENCH utilised TRENCH to WINCH utilised BELL-MOUTHS appropriate and in use COMMUNICATION Between personnel & with Winch Operator Visual / Hand Signals defined Radio (including mobile phone if appropriate) FREE SPOOLING FROM DRUM (e.g. not catching on drum side, drum free on cradle, etc.) Evidence of Hauling Tension (Main Location) HV Field. Drg. LV Field. Drg. Bending radius not compromised on corners Cable depth correct to facilitate guard at CHP COMMENTS:- |
| Approved Cable Hauling Auditor |
| Audited by |  | VEDN # |  |
| Signature |  | Date |  |

Part 5: Ad

for URD Projects

Part 4: Additional Requirements for URD & Option 2 UG Projects

The following additional requirements apply to all URD and Option 2 underground projects: A VEDN endorsed Worksite Civil (WC), Worksite Electrical (WE) or Network Auditor shall be engaged prior to the commencement of any VEDN related work associated with the electrical installation, e.g. any conduit installation. ALL civil and electrical assets (including road-crossing conduits) associated with the electrical installation shall be inspected by a VEDN endorsed auditor and as-built details recorded prior to being backfilled. A VEDN auditor shall verify that ALL civil and electrical assets associated with the electrical installation comply with the relevant Technical Standards, the approved construction drawing and any approved variations. (Variations may only be approved by the Network Owner Responsible Officer or the Council Officer responsible for Public Lighting as applicable.) Audit inspections shall be undertaken at the following project milestone points: Road-crossing conduit installation during initial road construction earthworks Trench & conduit inspection by a WE or Network Auditor prior to electrical installation to verify suitability After electrical installation prior to backfill Mandatory report items supported by measurements, photos and a tabulation of locations shall be provided as follows: Mains cable/conduit crossings above or below any other asset at ALL locations not accessible for excavation at the Powercor Final Audit, unless conclusive evidence can be provided that the crossing clearance exceeds 0.6m. This includes under road surfaces or other hard reinstatement areas, including footpaths, pram crossings and driveway crossovers. Mains cable/conduit under-crossings of any other asset exceeding 1.5m depth, i.e. the final surface cover/obvert depth of the electrical asset is 1.55m or more. HV cable or HV conduit bends of 45 degrees or greater - bending radius to be measured and recorded. In all cases above, a tabulation of locations with depth and clearance measurements (or bending radius measurement), together with clear photos must be provided. The client’s Electrical Project Manager is responsible to co-ordinate and ensure that all applicable locations have been identified. Any location that does not have information recorded will be deemed non-compliant subject to the required clearances being proven to the satisfaction of Powercor. Photo requirements: The photo locations and assets must be clearly identified/labelled and include a measurement scale in shot Photos to show clear and conclusive evidence and to be taken at the measurement point level Photos to be taken with a camera or smart phone with GPS location capabilities enabled and with the Latitude/Longitude co-ordinates or EXIF data included The photos and audit information are to be provided to the Electrical Project Manager (when appointed), who shall be responsible for uploading photo’s (>100kB <1MB) when submitting the Final Audit application The Civil and Electrical auditors shall be required to make additional declarations that ALL assets have been inspected at the nominated milestones and were compliant at the time of audit. Where multiple auditors have carried out inspections all must sign and the auditor who conducted the majority of inspections must sign as taking overall responsibility.

| DECLARATIONS |
| --- |
| Approved Worksite Civil Auditor(s) - if applicable |
| ALL underground civil works and conduits for the project electrical installation have been inspected and are compliant with the Technical standards, the approved construction drawing and approved Network Owner Responsible Officer variations (if applicable). The following auditors carried out the inspections on site. |
| Auditor Name |  | VEDN # |  |
| Signature |  | Date |  |
| Auditor taking Responsibility |  | VEDN # |  |
| Signature |  | Date |  |
| Approved Worksite Electrical or Network Auditor(s) |
| ALL underground civil and electrical works (strike out civil if not applicable) for the project electrical installation have been inspected and are compliant with the Technical standards, the approved construction drawing and approved Network Owner Responsible Officer variations (if applicable) at the time of inspection. The following auditors carried out the inspections on site. |
| Auditor Name |  | VEDN # |  |
| Signature |  | Date |  |
| Auditor Name |  | VEDN # |  |
| Signature |  | Date |  |
| Auditor taking Responsibility |  | VEDN # |  |
| Signature |  | Date |  |

Mandatory Report Item Locations

| Location | Assets | Clearance & Electrical Depth | Photo ID | Auditor Initials | Inspection Date |
| --- | --- | --- | --- | --- | --- |
| Outside Lot 36 | 150mm conduit/ 900mm SW drain | 340mm/0.85m | 15 |  |  |
| 7.8m West of lot 25/27 | 100mm conduit/ 200mm water pipe | 270mm/1.2m | 16 |  |  |
| Opposite lot 54 in Harris Rd | 150mm conduit/45 degree bend | 2.2m radius | 17 |  |  |